## Slide 1
Team Name: Drones for Tree Trimming
April 27th, 2021
Tyler Bryant, Darrell Fambro, Keith Liang, Nikhil Patel, Matthew Ramberger
Capstone Expo:
An Optimal Drone End-Effector for Vegetation Pruning

## Slide 2: Meet the Team
Matthew Ramberger [EE]
Darrell Fambro [CmpE]
Nikhil Patel [CmpE]
Keith Liang [EE]
Tyler Bryant [EE]
Testing Team Lead
Webmaster
Software Team Lead
Hardware Team Lead
Director of Communications

## Slide 3: Introduction
Goal: Design an optimal end effector configuration that integrates with a DJI Inspire Drone
  Optimal: Perform light trimming and pruning of vegetation surrounding power lines
  Able to withstand repetitive impact with grass and dirt from a height range of 30-50 feet
  The end effector will attach to a branch and disconnect from the drone, allowing the drone to safely fly away while the cut is made
DJI Inspire 1

## Slide 4: Motivation
Implement the use of drones to provide safer and more reliable services to customers
Florida Power & Light Aerial Intelligent Response (FPLAIR)
  Oversees all aerial inspections of the company’s overhead transmission and distribution facilities
  Percepto “Drone-in-Box” Solutions to aid in hurricane disaster recovery

## Slide 5: End-Effector Mechanical Assembly
Hardware Components
  L-Shaped aluminum core structure
  Ryobi BSH-120 Gardening Tool
  ACTOBOTICS Parallel Gripper Kit
  Flying Tech Payload Release Mechanism
  Lexan Polycarbonate Sheets
  Foam Cushioning
Aluminum Frame with Lexan
Aluminum Frame w/ support bars, cutter, and clamp
Finished End-Effector

## Slide 6: End-Effector Electrical Systems
Microprocessor
Accelerometer
Voltage Regulator (5V)
Battery Terminals
PCB Design
Two NPN BJT Transistors
Soldered Breadboard

## Slide 7: End-Effector Software Design
Communications between controller and end-effector are done using UART over bluetooth
  2 nRF52840 microcontroller development boards
The nRF52840 chip has a built-in bluetooth module capable of long ranges (> 200 ft)
The nRF52840-DK board transmits character based commands to the end-effector’s board (i.e. ‘!C’, ‘!T’, ‘!R’)
  Pressing a button triggers transmission (see right)
Transmitting controller software flow diagram
nRF52840-DK development board

## Slide 8: End-Effector Software Design
The nRF52840 Feather Express receives commands and parses them
  Toggles the clamp, cutter, and release accordingly by sending out the appropriate signal on a pin (see right)
Detects if the end-effector is stuck after being released from the drone using an accelerometer (i.e. in a tree)
  Releases clamp if no fall detected 30 sec after drone release
Receiving controller software flow diagram
nRF52840 Feather Express development board

## Slide 9: Drop Test Video
Drop Test #2: ~40 feet
Drop Test #1: ~20 feet
Results
Drop test was around 4 lbs - 1.5x our current weight
Framing easily survived both drops
Dirt getting inside frame is a problem

## Slide 10: Testing and Results
Weight ~ 2.5 pounds
Signal Range ~ 200-250 feet LOS
Battery Lifetime ~ 45-60 minutes
Fall Survival Height ~ Survived 40 Feet
Cutting Size ~.10’’ - .40’’
  Inconsistent over .40’’

## Slide 11: Future Steps
Additional release mechanism for vertical cuts
  Integrating release mechanisms inside frame
Upgrading soldered breadboard to printed circuit board
Increased diameter and power of cut potential
Adding shock absorbent mounting
Upgrading to titanium framing
Upgrading drone to increase payload capacity